## Slide 1: Transport Protocols in the Internet
Introduction to TCP
IN2140: Introduction to Operating Systems and Data Communication

## Slide 2: TCP - Transmission Control Protocol
TCP is the main transport protocol of the Internet
TCP provides
  Reliable end-to-end byte stream over an unreliable network service
Motivation: network with connectionless service
  Packets and messages may be
    duplicated, in wrong order, faulty
    i.e., with such service only, each application would have to provide recovery
      error detection and correction
  Network or service can
    impose packet length
    define additional requirements to optimize data transmission
    i.e., application would have to be adapted

## Slide 3: TCP Characteristics
Data stream oriented
  TCP transfers serial byte stream
  Maintains sequential order
Unstructured byte stream
  Application often has to transmit more structured data
  TCP does not support such groupings into (higher) structures within byte stream

## Slide 4: TCP Characteristics
Data stream oriented
  TCP transfers serial byte stream
  Maintains sequential order
Unstructured byte stream
  Application often has to transmit more structured data
  TCP does not support such groupings into (higher) structures within byte stream
Buffered data transmission
  Byte stream not message stream: message boundaries are not preserved
    no way for receiver to detect the unit(s) in which data were written
  For transmission the sequential data stream is
    Divided into segments
    Delayed if necessary (to collect data)

## Slide 5: TCP Characteristics
Virtual connection
  Connection established between communication parties before data transmission
Two-way communications (fully duplex)
  Data may be transmitted simultaneously in both directions over a TCP connection
Point-to-point
  Each connection has exactly two endpoints

## Slide 6: TCP State machine
CLOSED
LISTEN
SYN RCVD
SYN SENT
ESTABLISHED
FIN WAIT 1
FIN WAIT 2
CLOSING
TIME WAIT
CLOSE WAIT
LAST ACK
Send SYN
Recv SYN ACK
Send ACK
Send FIN
Recv ACK
Recv FIN Send ACK
Timeout
Send FIN
Recv SYN
Send SYN ACK
Recv FIN
Send ACK
Recv ACK
Timeout
Recv RST
Recv SYN Send SYN ACK
Send FIN
Recv FIN Send ACK
Recv FIN ACK
Send ACK
Recv ACK
Send SYN

## Slide 7: Typical State Sequence of a TCP Client
CLOSED
LISTEN
SYN RCVD
SYN SENT
ESTABLISHED
FIN WAIT 1
FIN WAIT 2
CLOSING
TIME WAIT
CLOSE WAIT
LAST ACK
Send SYN
Recv SYN,ACK
Send ACK
Send FIN
Recv ACK
Recv FIN, Send ACK
Timeout

## Slide 8: Typical State Sequence of a TCP Server
CLOSED
LISTEN
SYN RCVD
SYN SENT
ESTABLISHED
FIN WAIT 1
FIN WAIT 2
CLOSING
TIME WAIT
CLOSE WAIT
LAST ACK
Timeout
Recv SYN
Send SYN,ACK
Recv ACK
Recv FIN,
Send ACK
Send FIN

## Slide 9: TCP: Message Format
TCP/IP Header Format
Destination Address
Source address
Time to live
Protocol
Header checksum
Identification
D
M
Fragment offset
Version
IHL
Type of service
Total length
PRE
ToS
Data
Options
Source port
Destination port
Sequence number
Piggyback acknowledgement
THL
F
Window
S
R
P
A
U
unused
Checksum
Urgent pointer
Options (0 or more 32 bit words)
IP header
TCP header
Used for demultiplexing:
identifies connection
Used for demultiplexing:
service address for connection setup

## Slide 10: TCP Characteristics
Virtual connection
  Connection established between communication parties before data transmission
Two-way communications (fully duplex)
  Data may be transmitted simultaneously in both directions over a TCP connection
Point-to-point
  Each connection has exactly two endpoints
Reliable
  Fully ordered, fully reliable
    Sequence maintained
    No data loss, no duplicates, no modified data

## Slide 11: TCP in Use & Application Areas
Benefits of TCP
Reliable data transmission
  Efficient data transmission despite complexity
  Can be used with LAN and WAN for
    low data rates (e.g. interactive terminal) and
    high data rates (e.g. file transfer)
Disadvantages when compared with UDP
Higher resource requirements
  buffering, status information, timer usage
Connection set-up and disconnect necessary
  even with short data transmissions
Applications
everything on the Web including video-on-demand (http)
File transfer (scp, ftp)
Interactive terminal (ssh, telnet)
E-mail (smtp, imap)
X-Windows