## Slide 1: Transport layer
Flow Control
IN2140: Introduction to Operating Systems and Data Communication

## Slide 2: Flow Control on Transport Layer
Flow control mechanisms:
Stop-and-wait
Sliding window
  Go-back-N / no buffer allocation
  Selective repeat / static buffer allocation
  Credit mechanism / dynamic buffer allocation
Network
Layer
Transport
Layer
Application
Layer
Data Link
Layer
Physical
Layer
Fast sender shall not flood slow receiver
Link layer
Few connections (one per host)
Short distances
Transport layer
Potentially many connections (several per application)
Potentially long distances

## Slide 3: Flow control and error treatment
Problem
sender can send faster than receiver can receive
Without flow control
receiver loses packets despite error-free transmission
With flow control
sender can adapt to receiver’s abilities by feedback
Comment
error control and flow control are usually interlinked
rate control
  controls sending speed as well
  but defines sequencing of send operations
  whereas flow control defines conditions for next send operation
© Ralf Steinmetz, Technische Universität Darmstadt

## Slide 4: Transport layer
Flow Control: stop-and-wait
IN2140: Introduction to Operating Systems and Data Communication

## Slide 5: Flow control: Stop-and-Wait
sender
receiver
packet
ACK
packet
ACK
Needed:
(A) a receiving buffer
(B) bi-directional communication

## Slide 6: Flow control: Stop-and-Wait
sender
receiver
packet
ACK
Packets can get lost
sender
receiver
packet
ACK
packet
Features required by Stop-and-Wait:
fix the loss
distinguish packet loss and ACK loss

## Slide 7: Flow control: Stop-and-Wait
sender
receiver
packet
ACK
(a) fix the loss
packet
start a timer
timer expired
send packet again
start new timer
ACK arrived
cancel timer
Timeout interval:
Too short: unnecessary sending of packets
Too long: unnecessary long wait in case of error

## Slide 8: Flow control: Stop-and-Wait
sender
receiver
(b) distinguish packet loss and ACK loss
sender
receiver
packet 0
ACK
packet 0
packet 0 or
packet 1?
ACK
packet 0 or
packet 1?
ACK
packet 1 expected
packet 0
expected
packet 0
expected
packet 1 expected

## Slide 9: Flow control: Stop-and-Wait
sender
receiver
Distinguish cases by sequence number: single bit with value 0 and 1
sender
receiver
packet 0
expected
packet 0 expected
received
packet 1 expected
received
received 1
0
0
1
0
1
packet
ACK
packet
ACK
0
0
1
0
1
0
ACK
packet
packet
packet
ACK
packet
ACK
packet 1
expected
packet 0
expected
received 0
discard 0
packet 0 expected
packet 1 expected

## Slide 10: Flow control: Stop-and-Wait
Stop-and-Wait
sender can never send new packet before ACK or timeout
connection is idle most of the time
poor throughput
Gigabit Ethernet channel
transmission rate: 1 Gbps
roundtrip delay 200 (2*0.1 )
packet size: 8000 bit
in comparison  ACK is short and negligible
this means
sending takes 8000 bit / 1.000.000.000 bps = 8
sender is blocked for 192 of 200
 Channel utilization 4%
receiver
ACK
packet
sender
s
s

## Slide 11: Transport layer
Flow Control: sliding window
IN2140: Introduction to Operating Systems and Data Communication

## Slide 12: Flow control: Sliding Window
Improve utilization: pipelining
Flow control: sliding window mechanism
sender
receiver
packet 0
ACK 0
packet 1
packet 2
ACK 1
ACK 2
packet 8
ACK 8

## Slide 13: Sliding Window: Concept
1st goal of link flow control:
receiver buffer must not overflow
Assumptions:
each buffer can contain one packet
Two windows per communication relationship
Sender Window (or Send Window)
packets that were sent but not yet acknowledged
Receiver Window (or Receive Window)
packets that can be accepted
w
e
s
e
n
d
s
o
m
e
d
a
t
a
f
r
o
m
t
h
e
t
o
p
send
w
e
s
e
recv
buffers that fit into the current send window can be in flight at the same time
(“in flight”: sent but not acknowledged)
d
s
n
packets that fit into the current receive window
are considered valid and are acknowledged on arrival
packets are identified by sequence numbers
but the packets keep coming
and these numbers will wrap eventually
Notes: flood : overflomme

## Slide 14: Sliding Window: Concept
Sender
1
2
5
6
0
3
4
7
Example:
SeqNo: [0..7]
Window Size (WS): 3
lower bound
upper bound
advancing sender seqno (modulo 8)
LB: when ACK is received
UB: when sending a packet
Sender side
2 variables
LB
UB
0
0
LB: oldest seqno that is still unconfirmed
UB: next seqno to be sent
if LB==UB : nothing is in flight sender is idle
0
0

## Slide 15: Sliding Window: Concept
Sender
1
2
5
6
0
3
4
7
Example:
SeqNo: [0..7]
Window Size (WS): 3
lower bound
upper bound
LB: oldest seqno that is still unconfirmed
UB: next seqno to be sent
if LB==UB : nothing is in flight sender is idle
increase UB (modulo 8 !)
when sending a packet
Sender side
2 variables
LB
UB
0
0
send packet(0) packet(1) packet(2) WS=3
1
2
3
increase LB (modulo 8 !)
when receiving an ACK
recv ACK(0): WS=2
1

## Slide 16: Sliding Window: Concept
Sender
1
2
5
6
0
3
4
7
Example:
SeqNo: [0..7]
Window Size (WS): 3
lower bound
upper bound
LB: oldest seqno that is still unconfirmed
UB: next seqno to be sent
if LB==UB : nothing is in flight sender is idle
increase UB (modulo 8 !)
when sending a packet
Sender side
2 variables
LB
UB
send packet(0) packet(1) packet(2) WS=3
3
increase LB (modulo 8 !)
when receiving an ACK
recv ACK(0): WS=2
1
send packet(3) WS=3
4
recv ACK(1), ACK(2), ACK(3) WS=0
2
3
4
send packet(4) packet(5) packet(6) WS=3
5
6
7

## Slide 17: Sliding Window: Concept
Receiver
1
2
5
6
0
3
4
7
Example:
SeqNo: [0..7]
Window Size (WS): 3
lower bound
upper bound
LB: lowest valid seqno that should be ACKed
UB: lowest invalid seqno
if UB==LB: buffer full
if UB==(LB+3)%8: nothing to ACK
increase UB (modulo 8 !)
when sending an ACK
Receiver side
2 variables
LB
UB
0
recv packet(0) … WS=2
3
increase LB (modulo 8 !)
when receiving a packet
send ACK(0) WS=3
1
4

## Slide 18: Sliding Window: Concept
Receiver
1
2
5
6
0
3
4
7
Example:
SeqNo: [0..7]
Window Size (WS): 3
lower bound
upper bound
LB: lowest valid seqno that should be ACKed
UB: lowest invalid seqno
if UB==LB: buffer full
if UB==(LB+3)%8: nothing to ACK
increase UB (modulo 8 !)
when sending an ACK
Receiver side
2 variables
LB
UB
recv packet(0) … WS=2
increase LB (modulo 8 !)
when receiving a packet
send ACK(0) WS=3
1
4
recv packet(1) packet(2) packet(3) WS=0
5
6
7
2
3
4
send ACK(1) ACK(2) ACK(3) WS=3

## Slide 19: Transport layer
Flow Control: cumulative ACK
IN2140: Introduction to Operating Systems and Data Communication

## Slide 20: Sliding Window: Concept
Receiver
1
2
5
6
0
3
4
7
Example:
SeqNo: [0..7]
Window Size (WS): 3
Feature: Cumulative ACK
sender
receiver
Sender
1
2
5
6
0
3
4
7
LB
UB
0
0
LB
UB
3
0
packet 0
packet 1
packet 2
3
1
ACK 0
4

## Slide 21: Sliding Window: Concept
Receiver
1
2
5
6
0
3
4
7
Example:
SeqNo: [0..7]
Window Size (WS): 3
Feature: Cumulative ACK
sender
receiver
Sender
1
2
5
6
0
3
4
7
LB
UB
3
0
LB
UB
4
3
packet 0
packet 1
packet 2
ACK 0
ACK 1
ACK 2
ACK 0
3
6
3

## Slide 22: Sliding Window: Concept
Receiver
1
2
5
6
0
3
4
7
Example:
SeqNo: [0..7]
Window Size (WS): 3
Feature: Cumulative ACK
sender
receiver
Sender
1
2
5
6
0
3
4
7
LB
UB
6
0
LB
UB
6
3
packet 0
packet 1
packet 2
ACK 1
ACK 2
ACK 0
3
3
packet 3
packet 4
packet 5
6

## Slide 23: Sliding Window: Concept
Receiver
1
2
5
6
0
3
4
7
Example:
SeqNo: [0..7]
Window Size (WS): 3
Feature: Cumulative ACK
sender
receiver
Sender
1
2
5
6
0
3
4
7
LB
UB
3
0
LB
UB
7
3
packet 0
packet 1
packet 2
ACK 1
ACK 2
ACK 0
3
packet 3
packet 4
packet 5
6
ACK 5
ACK 3
ACK 4
6
0
1
4
6
Without cumulative ACKs:
timeout & retransmission
With cumulative ACKs:
ACK 5 confirms everything up to 5

## Slide 24: Sliding Window
Stored packets at the sender
the sender must store all unacknowledged packets and be able to retransmit
maximum number defined by sender’s window size (here 3)
the packets not yet acknowledged by the receiver
Stored packets at the receiver
not necessary to store any packets
  receive buffer must hold at least one packet, but can be passed to next layer right away
not useful to store more than one receiver window size
ACK sent by receiver only if the packet
has been identified as being correct
can be transmitted correctly to the application
  correct includes “in the right order”
  correct includes usually: free from detected bit errors

## Slide 25: Transport layer
Flow Control: retransmission
IN2140: Introduction to Operating Systems and Data Communication

## Slide 26: Sliding Window
Retransmission approaches
sender
receiver
packet 0
packet 1
packet 2
ACK 0
packet 3
packet 1
packet 2
ACK 3
ACK 1
packet 3
ACK 2
discard 2
discard 3
This approach is called
Go-Back-N
Receiver accepts packets only in order
Advantages:
receiver needs only buffer for 1 packet
if the network usually looses >1 packets in a row, this fixes the problem quickly
packet 4

## Slide 27: Sliding Window
Retransmission approaches
sender
receiver
packet 0
packet 1
packet 2
ACK 0
packet 3
packet 1
packet 2
ACK 3
ACK 1
packet 3
ACK 2
sender
receiver
packet 0
packet 1
packet 2
packet 3
packet 1
ACK 3
ACK 0
ACK 0
ACK 0
packet 4
packet 4
keep 2
keep 3

## Slide 28: Sliding Window
Retransmission approaches
sender
receiver
packet 0
packet 1
packet 2
packet 3
packet 1
ACK 3
ACK 0
ACK 0
ACK 0
packet 4
This approach is called
Selective Repeat
Receiver buffers packets that arrive out of order but in window
Advantages:
less traffic
if the network usually looses only 1 packet in a row, this uses bandwidth better
keep 2
keep 3