## Slide 1: Network layer
Routing
IN2140: Introduction to Operating Systems and Data Communication

## Slide 2: Network layer
Routing - repetition
IN2140: Introduction to Operating Systems and Data Communication

## Slide 3: Network Layer
Primary task from a layer model perspective
  To provide service to the transport layer
    Connectionless or connection-oriented service
    Uniform addressing
    Internetworking: provide transitions between networks
    Routing
    Congestion control
    Quality of Service (QoS)

## Slide 4: Routing
The main L3 task is
  enable data transfer from end system to end system
    several hops, (heterogeneous) subnetworks
    compensate for differences between end systems during transmission
The Intermediate Systems are often called Routers
intermediate system
network
end system
network
is sub-network (subnet) of
routing depends on actual connections between intermediate systems (routers)
in many case, the organization into subnetworks coincides with routing borders and provides clues
but it is not essential for routing
routing algorithms work on graphs

## Slide 5: Inside the Network Layer
An L3 packet includes
Version
DSCP
Flow label
Payload length
Next header
Hop Limit
Destination Address
(128 bit)
Source address
(128 bit)
IPv6 Header
L4 Data
ECN
headers and trailer to specify service requirements
in particular:
information required by intermediate systems for forwarding
for connectionless service:
end system address of the destination
for connection-oriented service:
route label
OR
virtual circuits require routing during connection setup
route label is used later
packet switching requires routing for every packet
destination address is used for every packet

## Slide 6: Network layer
Routing - foundations
IN2140: Introduction to Operating Systems and Data Communication

## Slide 7: Routing: Foundations
Task
  To define the route of packets through the network
    From the source
    To the destination system
Routing algorithm
  Defines on which outgoing line an incoming packet will be transmitted
Route determination
  Packet
    Routing algorithm makes individual decision for each packet
  Virtual circuit
    Routing algorithm runs only during connect (session routing)

## Slide 8: Routing: Routing and Forwarding
Incoming
lines
Outgoing
lines
Router
IS
ES
ES
ES
ES
selecting an outgoing line

## Slide 9: Routing: Routing and Forwarding
Distinction can be made
  Routing: makes decision which route to use
  Forwarding: what happens when a packet arrives
desti-
nation
link
A
0
B
2
C
1
D
2
Routing
Process
Topology, link utilization, etc.
information
Fills & Updates
Uses & Looks up
Data packets
Incoming
lines
Outgoing
lines
Forwarding
Process
Routing
table
Router

## Slide 10: Good Properties for Routing Algorithms
Correctness
Simplicity
  Minimize load of ISes
Robustness
  Compensation for IS and link failures
  Handling of topology and traffic changes
Stability
  Consistent results
  No volatile adaptations to new conditions
Fairness
  Among different sources compared to each other
Optimality

## Slide 11: Routing Algorithms: Conflicting Properties
Often conflicting: fairness and optimization
Some different optimization criteria
  average packet delay
  total throughput
  individual delay
    conflict
Example:
  communication among a  A, b  B, c  C uses full capacity of horizontal line
  optimized throughput, but
  no fairness for x  X – Tradeoff between fairness and optimization
Therefore often
  hop minimization per packet
    it tends to reduce delays and decreases required bandwidth
    also tends to increase throughput
a
A
IS
IS
b
B
IS
IS
c
C
IS
IS
x
X

## Slide 12: Classes of Routing Algorithms
Class: Non-adaptive Algorithms
  Current network state not taken into consideration
    Assume average values
    All routes are defined off-line before the network is put into operation
    No change during operation (static routing)
  With knowledge of the overall topology
    Spanning tree
    Flow-based routing
  Without knowledge of the overall topology
    Flooding
Class: Adaptive Algorithms
  Decisions are based on current network state
    Measurements / estimates of the topology and the traffic volume
  Further sub-classification into
    Centralized algorithms
    Isolated algorithms
    Distributed algorithms
[Inkowik@wikipedia, CC BY SA 2.0]
[Ingolfsson@wikipedia]
Notes: Inkowik@wikipedia -

## Slide 13: Optimality Principle and Sink Tree
Starting idea: using a route has a cost
  number of hops, delay, …
General statement about optimal routes
  if router J is on the optimal path from router I to router K
  then the optimal path from router J to router K uses the same route
Idea of the proof
  best route from I to K is like this:
    r1: from I to J, then
    r2: from J to K
  then r2 is also the best route from J to K
  if better route r3 from J to K would exist
    then concatenation of r1 and r3 would improve route from I to K
Set of optimal routes
  from all sources
  to a given destination
  form a tree rooted at the destination: Sink Tree
I
J
K
r1
r2
r3

## Slide 14: Sink Tree
B
C
J
E
D
F
K
M
L
I
N
O
H
Sink Tree for Destination B
A
G
D
H
I
E
B
C
J
F
K
L
M
N
O
B
0
A
1
C
1
F
2
D
2
I
2
J
2
N
3
H
3
E
3
G
3
K
3
L
4
O
4
M
4

## Slide 15: Sink Tree
Sink Tree for Destination B
[Adrian Michael@Wikipedia, CC BY 3.0]
B

## Slide 16: Sink Tree
Comments
  tree: no loops
    each optimal route is finite with bounded number of hops
  not necessarily unique
    other trees with same path lengths may exist
Goal of all routing algorithms
  discover and use the Sink Trees for all routers
Not realistic to use Sink Trees as real-life routing algorithm
  need complete information about topology
  Sink Tree is only a benchmark for routing algorithms
Sink Tree for
Destination B
B
C
J
E
D
F
K
M
L
I
N
O
H
A
G
D
H
I
E
B
C
J
F
K
L
M
N
O

## Slide 17: Methodology & Metrics
Compute the shortest path between a given pair of routers
Different metrics for path lengths can be used
  can lead to different results
  sometime even combined
Metrics for the "ideal" route, e.g., a "short" route
  number of hops
  geographical distance
  bandwidth
  average data volume
  cost of communication
  delay in queues
  ...