## Slide 1: Network layer
Distributed Routing:
Distance Vector Routing
IN2140: Introduction to Operating Systems and Data Communication

## Slide 2: Distance Vector Routing
Principle
every IS maintains a table (i.e., vector) stating
  best known distance to destinations
  and line to be used
ISes update tables
  by exchanging routing information with their neighbors

## Slide 3: Distance Vector Routing
Each IS
  maintains routing table with one entry per router in the subnet
  is assumed to know the distances to each neighbor
  sends list with estimated distances to each destination periodically to its neighbors
X receives list E(Z) from neighbor Y
  Distance X to Y: e
  Distance Y to Z: E(Z)
  Distance X to Z via Y: E(Z)+e
IS computes new routing table from the received lists containing
  Destination IS
  Preferred outgoing path
  Distance

## Slide 4: Distance Vector Routing
Previous routing table will not be taken into account
  Reaction to deteriorations
A
B
C
D
E
F
G
H
I
J
K
L
A
0
B
12
C
25
D
40
E
14
F
23
G
18
H
17
I
21
J
9
K
24
L
29
A
24
36
18
27
7
20
31
20
0
11
22
33
I
20
31
19
8
30
19
6
0
14
7
22
9
H
21
28
36
24
22
40
31
19
22
10
0
9
K
28
20
17
30
18
0
15
8
A
20
A
I
H
I
I
H
12
H
10
I
-
6
K
K
line
JA
8
delay
JI
10
JH
12
JK
6

## Slide 5: Distance Vector Routing
Fast route improvement
Fast distribution of information about new short paths (with few hops)
A
B
C
D
E
∞
∞
∞
∞
1
∞
∞
∞
1
2
∞
∞
1
2
3
∞
1
2
3
4
Example
  initially A unknown
  later: A connected with distance 1 to B, this will be announced
  Distribution proportional to topological spread
  Synchronous (stepwise) update is a simplification

## Slide 6: Distance Vector Routing
Slow distribution of information about new long paths (with many hops)
“Count to Infinity” problem of DVR
Example: deterioration
  Here: connection destroyed
  A was previously known, but is now detached
  The values are derived from (incorrect) connections of distant IS
Comment
  Limit "infinite" to a finite value, depending on the metrics, e.g.
    ‘infinite’ = maximum path length+1
A
B
C
D
E
∞
∞
∞
∞
1
2
3
4
3
2
3
4
3
4
3
4
5
4
5
6
5
6
5
6
7
6
7
6
7
8
7
8

## Slide 7: Distance Vector Routing
Variant: ‘Split Horizon Algorithm’
Objective: improve the "count to infinity" problem
Principle
  In general, to publicize the "distance" to each neighbour
  If neighbor Y exists on the reported route, X reports the response "false" to Y
    distance X (via Y) according to arbitrary i: 
Example: deterioration (connection destroyed)
  B to C: A =  (real), C to B: A =  (because B is on path to A), ...
But: still poor, depending on topology, example
  Connection CD is removed
  A receives "false information" via B
  B receives "false information" via A
    Slow distribution (just as before)
A
B
C
D
E
1
2
3
4
∞
2
3
4
∞
∞
3
4
∞
∞
∞
4
∞
∞
∞
∞
A
B
C
D